## Slide 1
CSE 4124
Digital System Design
Verilog Programming

## Slide 2
Introduction
Verilog HDL is a Hardware Description Language (HDL)
HDL is a language used to describe a digital system,
computer or a component of a computer.
for
example,
a
Most popular HDLs are V(VHSIC)HDL and Verilog
Verilog programming is similar to C programming
VHDL programming is similar to PASCAL (some say
Is an IEEE standard
like
Ada)

## Slide 3
Levels of description
Switch Level
Layout of the wires, resistors and transistors on an Integrated Circuit (IC)
chip
Gate (structural) Level
Logical gates, flip flops and their interconnection
RTL (dataflow) Level
The registers and the transfers of vectors of information between registers
Behavioral (algorithmic) Level
Highest level of abstraction
Description of algorithm without hardware implementation details (like C
programming)

## Slide 4
Levels of
description
Behavioral level
Easiest to write and debug, not synthesizable
Register Transfer Level
synthesizable
Uses the concept of registers (a set of flipflops) with combinational logic between them
Structural level
Very easy to synthesize
A text based schematic entry system

## Slide 5
Why Use HDL?
NO OTHER CHOICE:
For large digital systems, gate-level design is unmanageable
Millions of transistors on a digital chip
HDL offers the
large designs
mechanism
to
describe,
test
and
synthesize

## Slide 6
Verilog language
Describe a system by a set of modules (equivalent to functions in C)
Keywords, e. g., module, are reserved and
Verilog is case sensitive
in all lower
case
letters
Operators
(some examples)
Arithmetic: +, - ! ~ * /
Binary operators: &, |, ^, ~, !
Shift: << >>
Logical: &&, ||
Relational: <, <=, >,
>=, ==, !=
Identifiers
Equivalent to variable names
Identifiers can be up to 1024 characters.
Comments start with a "//" for one line or
/* to */ across several lines

## Slide 7
Number representation
Numbers are specified in the traditional form of a series
without a sign but also in the following form
<size><base format><number>
<size>: number of bits (optional)
of digits with or
<base format>: is the single character ' followed by one of the following
characters b, d, o and h, which stand
respectively.
<number>: contains digits which are
for binary, decimal, octal and
hex,
legal for the <base format>
Examples
549
'h 8FF
'o765
4'b11
3'b10x
5'd3
-4'b11
//
//
//
//
//
//
//
decimal number
hex number
octal
4-bit
3-bit
5-bit
4-bit
number
binary number 0011
binary number with the least significant bit unknown
decimal number
two's complement of 0011, or equivalently 1101

## Slide 8
Data types
Variables of type wires (wire) and registers (reg).
Register variables store the last value that was procedurally
assigned
Wire variables represent physical connections between structural
entities such as gates (Does not store anything, only a label on a wire)
The reg and wire data objects may have the following possible values:
0
1 x z
logical zero or false
logical one or true
unknown logical value
high impedance of tri-state gate
“reg” variables are initialized to 0 at the start of the simulation.
“wire” variable not connected to something has the x value.
NOTE: A variable of type register does not necessarily represent a physical register

## Slide 9
Boolean
operators
•
Bitwise operators perform bit-oriented operations on vectors
• ~(4’b0101) = {~0,~1,~0,~1} = 4’b1010
• 4’b0101 & 4’b0011 = {0&0, 1&0, 0&1, 1&1} = 4’b0001
Reduction operators act on each bit of a single input vector
•
•
&(4’b0101) = 0 & 1 & 0 & 1 = 1’b0
•
Logical operators return one-bit
(true/false)
results
•
!(4’b0101) = 1’b0
Bitwise
Logical
Reduction
returns x when x
Note distinction between ~a and !a
when operating on multi-bit values
&a
AND
~&a
NAND
|a
OR
~|a
NOR
^a
XOR
~^a
^~a
XNOR
!a
NOT
a && b
AND
a || b
OR
a == b a != b
[in]equality
or z in bits. Else returns 0 or 1
a === b a !== b
case [in] equality returns 0 or 1
based on bit by bit
comparison
~a
NOT
a & b
AND
a | b
OR
a ^ b
XOR
a ~^ b a ^~ b
XNOR

## Slide 10
Other
operators
Arithmetic
Conditional
Relational
a > b
greater than
a >= b
greater than or equal
a < b
Less than
a <= b
Less than or equal
a ? b : c
If a then b else c
-a
negate
a + b
add
a - b
subtract
a * b
multiply
a / b
divide
a % b
modulus
a ** b
exponentiate
a << b
logical left shift
a >> b
logical right shift
a <<< b
arithmetic left shift
a >>> b
arithmetic right shift

## Slide 11
#
operators
# operator that can have many different meanings depending
on the context of where it is being used .
Normally, # is used to represent a delay and the expression
that follows it is the amount of delay.
Again you need to see the context to know if 1 represents 1 nanosecond,
1 second, or something else.

## Slide 12
Program structure
A digital system as a set of modules
Each module has an interface to other module
(connectivity)
GOOD PRACTICE: Place one module per file (not a requirement)
Modules run concurrently
Usually there
modules
is
a
top
level
module
which
invokes
instances
of
other

## Slide 13
Module
Represent bits of hardware ranging from simple
systems, e. g., a microprocessor
gates
to
complete
Specified behaviorally, RTL, or structurally
The
structure of a module is the following:
module <module name> (<port list>);
<declarations>
<module items>
endmodule
<module name>
is an identifier that uniquely names the module.
<port list>
is a list of input, inout and output ports which are used to connect to other modules.
<declarations>
section specifies data objects as registers, memories, and wires as wells as procedural constructs such as functions and tasks
<module items>
may be initial constructs, always constructs, continuous assignments or instances of modules

## Slide 14
example: NAND gate
Here
is an RTL specification of a module
NAND
// Behavioral model of a NAND gate
module NAND(in1, in2, out);
input in1, in2;
output out;
// continuous assignment statement
assign out = ~(in1 & in2);
endmodule
Default: All undeclared variables are wires
and
are one
bit wide!
GOOD PRACTICE: Declare all variables

## Slide 15
Explanation of NAND module
The ports in1, in2 and out are labels on wires.
The continuous assignment “assign” continuously watches for changes
to variables in its right hand side and whenever that happens the right hand side is re-evaluated and the result immediately propagated to the left hand side (out).
The continuous assignment statement is used to model combinational
circuits where the outputs change when
one
wiggles
the
input.
// Behavioral model of a NAND gate
module NAND(in1, in2, out);
input in1, in2;
output out;
// continuous assign statement
assign out = ~(in1 & in2);
endmodule

## Slide 16
Instance of a module
The general form to invoke an instance of a module is:
<module name> <parameter list> <instance name> (<port list>);
<parameter list> are values of parameters passed to the instance
<instance name> identifies the specific instance of the module
An example parameter passed would be the delay for
a
gate
We will not use parameter list in this course!
For our purposes, to invoke an instance of a module
<module name> <instance name> (<port list>);

## Slide 17
Structural example: AND
gate
//Structural model of AND gate
from
two
NANDS
module AND(in1, in2,
input in1, in2;
output out;
out);
wire w1;
// two instances of
NAND NAND1(in1,
the module
in2, w1);
NAND
NAND NAND2(w1, w1, out);
endmodule
This module has two instances
of the
NAND module
called
NAND1
and NAND2 connected together by an internal wire w1.

## Slide 18
More
structural examples
module SRLatch(S, R, Q, Qbar);
input S, R;
output Q, Qbar;
NAND nand1(S, Qbar, Q);
NAND nand2(R, Q, Qbar);
endmodule
module DLatch(Clk, D, Q, Qbar);
input Clk, D;
output Q, Qbar;
wire S, R;
NAND nand1(D, Clk, S);
NAND nand2(~D, Clk, R);
SRLatch srlatch1(S, R, Q, Qbar);
endmodule
module DFlipFlop(Clk, D, Q, Qbar);
input Clk, D;
output Q, Qbar;
wire Qint, Qbarint;
DLatch dlatch1(~Clk, D, Qint, Qbarint);
DLatch dlatch2(Clk, Qint, Q, Qbar);
endmodule

## Slide 19
Continuous vs. procedural assignments
Continuous statement is used to model combinational logic
Continuous assignments drive wire variables
Evaluated and updated whenever an input operand changes value
Procedural assignment changes the state of a register
Used for both combinational and sequential logic
All procedural statements must be within “always” block
Example
This
is
combinational
logic
reg A;
always @ (B or C) begin
A = B & C;
end

## Slide 20
Events
The execution of a procedural statement is triggered
A value change on a wire
The occurrence of a named event
by:
always @ (B or C) begin // controlled by any value change in B or C
X = B & C;
end
always @(posedge Clk) Y <= B&C;
// controlled by positive edge of Clk
always @(negedge Clk) Z <= B&C;
// controlled by negative edge of Clk

## Slide 21
Model of a D-Flip flop
What is the behavior of a D-flipflop ?
During every positive clock edge, the input is transferred to the output
RTL model
module Dflipflop(D, Clk, Q, Qbar);
input D, Clk;
output Q, Qbar;
reg Qint;
// always is a procedural construct
// any assignment may be made only to registers always @(posedge Clk) Qint <= D;
assign Q = Qint;
assign Qbar = ~Qint;
endmodule

## Slide 22
Register sizes and assignments
Size of
reg
wire
reg
a register or
[0:7] A, B;
[0:3] Dataout;
[7:0] C;
wire in the declaration
// A and B are 8-bit wide with most significant bit as
// Dataout is a 4-bit wide
0th
bit
// C is a 8-bit register with most significant bit as the
// This will be the convention adopted in this course!
8th
bit
Assignments and concatenations
A = 8'b01011010;
B = {A[0:3] | A[4:7], 4'b0000};
B is set to the first four bits of A bitwise or-ed with the last four bits of A
and then concatenated with 0000. B now holds a value of 11110000.
{} brackets means the bits of the two or more arguments separated by
commas are concatenated together.

## Slide 23
Control constructs
Two control constructs
are
available:
case (<expression>)
<value1>:
begin
<statement>;
end
begin
<statement>;
end
<statement>;
endcase
if (A == 4)
begin
B = 2;
end
else
if (A == 2)
begin
B =
end
1;
else
begin
B =
end
4;
<value2>:
Default:

## Slide 24
Control statement examples
1-bit 2-to-1 multiplexer
module mux1bit2to1(a, b, s, out);
input a, b, s;
output out;
assign out = (~s & a) | (s & b);
endmodule
Another way to describe
module mux1bit2to1(a, b, s, out);
input a, b, s;
output out;
reg out; // used in procedural statement
always @ (s or a or b)
if (s == 0) out = a;
else out = b;
endmodule

## Slide 25
Blocking/Non-blocking
procedural assignments
Blocking assignment statement
// testing blocking and non-blocking
// assignment
module blocking(Clk, A, B);
input Clk;
output [7:0] A, B;
(= operator) acts much like
traditional programming languages
in
The whole statement is done before control passes on to the next
statement.
reg [7:0] A, B;
// as these will be used in
// procedural blocks
Non-blocking (<= operator)
Evaluates all the right-hand sides for the current time unit and
reg [7:0] C, D; // two internal registers
always @(posedge Clk) begin
// blocking procedural
// assignment
C = C + 1; A = C + 1;
assigns the left-hand sides at
end of the time unit.
the
Example: During every
clock
cycle
// non-blocking procedural
// assignment
D <= D + 1; B <= D + 1;
A is ahead of C by 1
B is same as D
end
endmodule

## Slide 26
Some tips
Declare ALL variables
An undeclared variable is treated as a wire!
Declare one variable (especially input/output)
per line
Provide comments for each of those variables
It will be helpful when you design complex modules
All modules must have the port list defined in the homework/projects